## Slide 1
Team 205: Robotic Arm to Assist Motorized Chair Users
Sponsor: Mr. Keith Van Houten, PPMD
Team Members: Brooke Harrington, Justin Lee, Cavan Moriarty, Omar Abuljobain, Andrew Baum
Faculty Advisors: Mr. Stephen Moyer, Mr. Jim Hess
Duchenne muscular dystrophy (DMD) is a progressive disorder that deteriorates muscles over time.
Users with DMD often require the use of motorized wheelchairs (Permobil M3)
People with DMD have limited range of motion (ROM) and often require a caretaker or robotic device to help with everyday tasks
Waveshare Ro-Arm
Waterproofing
Complete Two High Value Functions
Push an ADA compliant elevator button
Retrieve and return a drink to and from the user from a user programmed location
Background
Mounting
Conclusions
Problem Statement
Customer Needs
Current assistive devices are too expensive, cover a large footprint, and are difficult for people with DMD to control.
People with DMD would benefit from a simple to control, affordable robotic aid that executes specific high value functions.
Possible better robot arm choices – more research
Refined case design
Reworked electronics: different microcontroller and printable circuit board instead of protoboard
Completes high value functions and meets user requirements
Affordable at < $2,000
Compatible mounting with Permobil wheelchair
Open source – GitHub
The Werth Family and the Team at PPMD
Mr. Jim Hess,
Mr. Stephen Moyer,
Mr. Rick and Ms. Kristie from QL+
Recommendations &
What we’d do differently
Team Testing
Test | Results / Outcome
End Effector Load Capacity | 0.5 kg at max distance 0.6 kg at min distance
Verification of Safety Measures | Stayed within designated 300° of rotation
Joystick-Robot Accuracy | X Failed team standards Met ADA standards
Installation Time | 58.52 sec
Maintenance Time | 22 min 5 sec
End User Testing
Protoboard
1 joystick (3 axis, 2 buttons)
2 switches for system & joystick enable
5 buttons for stored functions/location
Team 205 meeting with Colin Werth for testing
  Special
  Thanks!
Images
Mounting Assembly Features:
Locking pin
Vertical and horizontal adjustment
Easy tightening
French cleat system
GitHub
End User Comments:
Move the joystick closer to the edge to be in line with the armrest
Joystick with twisting motion may not be ideal for people with DMD
End-effector tip requires non-slip material for button pressing
Armrest attachment for additional support
End-effector cover protects wrist servo
Sleeve protects elbow and base servo
Well protects internal electronics
Safety – Robot doesn’t hit user or other people | System withstands rainfall whilst maintaining normal operation
Ease of assembly, installation, and maintenance | Easily portable and self-contained for travel
Intuitive Controls that are like controls found on the wheelchair | Attached system fits through ADA compliant doorframe
Affordability (current market solutions >$60,000) | Ability to save custom, frequently-visited locations using buttons
Colin testing:
Mounting position
User interface
Retrieving a drink
Ergonomics
Fitting through an ADA compliant door
Team testing:
Accuracy of robot to hit elevator button
End effector slipping
Visibility, ease of maneuverability
GitHub Information
    Code
    CAD Files
    Tutorials
For others to reproduce our project and expand upon our work
Control Panel